## Slide 1
WEEKLY PROGRESS · 9 AUGUST 2026
Delta action models on 473 real dab repetitions
Fixed the capture pipeline, measured where the sim-to-real gap actually is, and found that ASAP's 4-DoF choice is right, for a reason the paper does not give.

## Slide 2
SUMMARY
Four things happened this week
1
Fixed three bugs in the capture data
29 mm pose error · 1.8% timebase drift · 83 mm height offset
2
Measured where the sim-to-real gap is
All four ankle joints, 4.79x worse than everything else
3
4-DoF delta model beats the full 23-DoF one
The full model cheats. Replicated across two training seeds.
4
Fine-tuned a policy, and it cannot balance
Two causes found. Neither is fixed yet.
ASAP publishes no working code for steps 2, 3 or 4 of its own pipeline. All three were written this week.

## Slide 3
RESULT 0 · THE DATA
The capture data had three bugs in it
1
Pose solver mis-centred on partial frames
29 mm position jump whenever a marker dropped
2
Frame rate stored as a float, then truncated
48.88 became 48. A 1.8% timebase drift.
3
Marker cluster used as the pelvis origin
Every root height 83 mm too low
All three fixed, verified, and pushed
Bug 1 is explained over the next two slides. Bug 2 is the dangerous one: a wrong timebase is invisible in the training loss, and only shows up when the data is round-tripped back.

## Slide 4
BUG 1 EXPLAINED · PART 1
How the pose solver works
Four markers sit on the pelvis. The solver works out how the pelvis has turned, by comparing the shape it sees now against the shape it recorded at the start.
Two shapes, different place and angle
recorded
seen now
Blue is the shape recorded at the start.
Orange is what the cameras see now.
Step 1: slide them onto the same centre
same centre, still turned
This removes WHERE the robot is.
It does not measure any turning.
Step 2: search for the turn that fits
orange sits inside blue
Try every rotation, keep the one that
lines the markers up. That is the answer.
Subtracting the centre does not measure the turn. It removes position, so that the turn is the only thing left to find.
The markers are bolted to the pelvis, so they never move relative to each other, and their average is a fixed point on the body.
Subtract it from every marker and the robot could be anywhere in the room, the numbers would be identical. Only turning changes them.
All of this holds only while all four markers are visible

## Slide 5
BUG 1 EXPLAINED · PART 2
What went wrong
dropped
centre moves 29 mm
Lose a marker and the centre of what is left
is no longer the same point on the body.
The two shapes ended up measured
about centres 29 mm apart
Fix: re-centre the recorded shape
on the markers that remain
predicted 29.08 mm measured 29.08 mm
after the fix: 0.38 mm
With all four markers visible nothing changes, so 67,427 full frames came out bit-identical.

## Slide 6
BUG 2 EXPLAINED
A frame rate that was quietly rounded down
we record at 48.88 Hz
ASAP rounds it DOWN
played as 48 Hz
real
ASAP
Over one whole dab, 298 frames or 6.1 seconds:
stored as 48
5.4 frames behind
stored as 49
0.7 frames off
Caught by asking for frames back
Ask for frame 250, get 245. The drift, mid-dab.
Asked for | Got back
10 | 10
100 | 98
250 | 245
Fix: store the rate as a whole number, 49
A wrong clock never shows up in a training curve. Only asking for the data back reveals it.

## Slide 7
BUG 3 EXPLAINED
Measuring from the wrong point on the body
PELVIS
83 mm
what the simulator wants ● above
what the cameras report ● below
The same height, measured two ways
How high is the pelvis above the floor?
 | height
From the robot's own joint angles | 0.767 m
From the cameras | 0.684 m
Difference | 0.083 m
Same distance, but measured to two different points
on the body. The gap between them is the offset.
Fix: shift by that 83 mm, turned with the body
Both capture sessions gave the same answer to within 1 mm, which is what makes it a fixed offset rather than noise.

## Slide 8
HOW THE NUMBERS ARE MADE
Measuring the gap: replay real actions in simulation
REAL ROBOT
473 dab reps recorded
initial state s₀
where the sim starts
actions aₜ
what we commanded
states sₜ
what the robot did
SIMULATOR
start at s₀, then apply aₜ
sim states ŝₜ
| ŝₜ − sₜ | per joint
= THE GAP
same start, same actions
The sim is reset to the robot's real state first, so both start from the same place.
Then the same actions go into both. Any difference after that is the simulator being wrong.
Re-anchored every 1.0 s, so small errors cannot pile up and look like a physics gap.

## Slide 9
RESULT 1
The gap is the ankles, and almost nothing else
Error as a share of each joint's own range of motion
L_AnklePitch
43.2%
L_AnkleRoll
25.0%
R_AnklePitch
21.3%
R_HipRoll
20.6%
R_AnkleRoll
15.4%
L_HipYaw
10.9%
L_HipPitch
7.1%
L_Knee
3.5%
L_ShoulderPitch
2.8%
All four ankle joints land in the top six. On average they are 4.79x worse than every other joint.
Why measure it this way
Each bar is one joint's full travel.
Red is how wrong the simulator is.
L_AnklePitch moves 25°
off by 11.0° of 25° = 43%
L_ShoulderPitch moves 135°
off by 3.8° of 135° = 3%
Same size error in degrees
means very different things
The paper asserts the G1's parallel-linkage ankle is the problem. This measures it, on our robot, before fitting anything.

## Slide 10
THE KEY IDEA
Why correcting 4 joints beats correcting 23
The delta model is scored mostly on WHERE THE BODY IS (weight 3.0), barely on joint angles (0.5). That leaves a shortcut.
23 DoF free to correct
Hip
Knee
Ankle
all free → many ways to place the pelvis
Bends the KNEE to put the body in the right place
Body position ✓
Ankle still wrong ✗
4 DoF free (ankles only)
Hip
Knee
Ankle
locked → only one way to place the pelvis
Must actually fix the ANKLE to place the body
Body position ✓
Ankle fixed ✓
The leg is kinematically redundant: many hip/knee/ankle combinations put the pelvis in the same place. Constraining the model removes the shortcut and forces it to model the real physics.

## Slide 11
RESULT 2
4 DoF wins. 23 DoF is worse than no correction at all.
Delta model | Joint error @1 s | Knee error | Verdict
No correction (baseline) | 2.49 deg | 1.00 deg | 
4-DoF, ankles only | 1.46 deg | 0.99 deg | best
23-DoF, seed 1 | 3.30 deg | 7.95 deg | worse than nothing
23-DoF, seed 2 | 3.10 deg | 3.74 deg | worse than nothing
Look at the knees. That is the cheating, visible as a number.
The 4-DoF model leaves them at 0.99 deg against a 1.00 deg baseline: untouched, because it cannot touch them.
Both 23-DoF seeds wreck them (7.95 and 3.74) while fixing the ankles only half as well.
The paper picks 4 DoF because it lacked data. We have the data it says is needed, and 4 DoF still wins.

## Slide 12
A TRAP WORTH KNOWING
Training reward picks the wrong model
Run | Training reward | Error vs the real robot | Verdict
23-DoF seed 2 | 5.34 ← highest | 3.10° | 2nd worst
23-DoF seed 1 | 4.82 | 3.30° | worst
no delta at all | — | 2.49° | 
4-DoF ankles | 4.78 ← lowest | 1.46° | best
Reward says seed 2 is the best run. Replay against the real robot says it is nearly the worst.
Both 23-DoF models are worse than applying no correction at all.
Choosing a checkpoint by reward, the normal thing to do, picks the wrong one.
Reward is measured in simulation. Quality can only be measured against the real robot.

## Slide 13
RESULT 3 · THE PROBLEM
Why the fine-tuned policy falls over
The delta model is deleted at deployment. The policy was never trained without it.
IN TRAINING
POLICY
ankle 0.51
DELTA MODEL
ankle 1.07
TOTAL 1.58
into the ankles
policy learns to balance
in THIS world
AT DEPLOYMENT
POLICY
ankle 0.51
DELETED
TOTAL 0.51
32% of training
falls over
The delta was supposed to be a small correction. It became a co-controller.
Its penalty term, exp(−||Δa||), goes flat once the correction is large, so nothing pulls it back down.
The correction grew from 3.7 to 10.7 during training, with the penalty reading exactly zero.

## Slide 14
WHERE THINGS STAND
Solid, and not solid
SOLID
Capture pipeline fixed and validated
473 reps, 140,821 frames, fully reproducible
Sim-to-real gap measured
ankles 4.79x, reproduces to ~1%
4-DoF beats 23-DoF
two seeds, independent evaluation samples
NOT SOLID
No deployable policy yet
both fine-tuned policies fall over in MuJoCo
Simulation cannot pick between them
each policy wins in the simulator it trained in
Only one motion tested
a standing, arm-heavy dab
v6 remains the only policy validated on hardware. Nothing on the robot has changed this week.

## Slide 15
NEXT
Three things, in order
1
Shrink the delta model
Replace exp(−||Δa||) with a penalty that does not go flat, so the correction stays a correction.
Nothing else works until the delta is small enough to remove safely.
2
Re-fine-tune against the smaller delta
Then check it in MuJoCo. That is the gate. Nothing goes on the robot until it passes.
3
Hardware A/B against v6
The only test that answers whether any of this transfers. Needs robot time.
Domain randomisation was tried this week and made the dependence worse, not better. It is not the fix.